SAE automations level(s)

0→ No automation
1→ Driver assistance: up to 2 functions automatized
e.g. diriving lane assistant
2→ Conditional automation: presence/authority of the driver still requires

3→
very strange authonomy level.

4→ High Automation:

5→ High Automation everywhere:

Sensor(s)

RADAR: Already used

SONAR: Already used

Vision: very dense information content. It is a passive sensor
- computational limit
- Vislab 30 fps, 4k(4000 pixels) high resolution camera [4 cameras ]
- “Sun-stressed” conditon solvable
  VISLAB: stereo camera 30cm arm => disparity image. color gradient identifies distance of the object(s).

PROS: high ingormation density
CONS: requires calibration (especially in stereo mode) and must be maintained for years!
=> Vislab fa calibrazione online (‘on the flight’) via features extraction!

LiDAR: it cost too much => new technology is more compact, not mechanical, cheaper
- assumed range is 20m
- installed in front of the car not appreciated by designer, if installed in front of the car up to 120° FoV but more than 1 might be needed.

PROS: works at night
CONS: low density

Technology

5G: could be useful to see vehicles at 5km distance
  - Not a strict pre-requisite

MAPS: many AD vehicles rely on maps

1. Algorithms: three levels
  1. perception
  2. Decision
  3. actuation

Physical perception:
can be solved through sensors

Behavioural perception:
- predict behaviour of other vehicles / pedestrians
  e.g. another driver makes a sign like: “ti lascio passare”
- DL plays a big role here.